## Slide 1
Department of Computer Engineering
1
Sequential Logic Design – Truth Tables and Excitation Tables

## Slide 2: Points covered
Department of Computer Engineering
2
Introduction
JK Flip flop

## Slide 3: Department Vision & Mission
Department of Computer Engineering
Vision
Achieve academic excellence through education in computing, to create intellectual manpower to explore professional, higher educational and social opportunities.
Mission
To impart learning by educating students with conceptual knowledge and hands on practices using modern tools, FOSS technologies and competency skills there by igniting the young minds for innovative thinking, professional expertise and research.

## Slide 4
SR FF
IF S=R=0 Circuit will be same state i.e. No Change.
IF S=1 & R=0 then Q=1
IF S=0 & R=1 then Q=0
IF S=R=1 , then both the outputs Q and Q̅ will try to become 1 which is not allowed and therefore this input condition is prohibited
(Race Condition).
Department of Computer Engineering

## Slide 5: JK FF
Used to avoid race condition which does occur in SR FF
It has 2 inputs named J & K.
It has two outputs Q & Q’.
One Clock signal.
2 Asynchronous inputs PR & CLR
Symbol of JK -
Department of Computer Engineering

## Slide 6
JK FF Operation
J | K | Q | Q’ | Mode
0 | 0 | Q | Q’ | Hold
1 | 0 | 1 | 0 | Sets
0 | 1 | 0 | 1 | Resets
1 | 1 | Q’ | Q | Toggle
The 4 modes of operation are: hold, set, reset, toggle
Truth Table of JK
Department of Computer Engineering

## Slide 7
D-Type Flip Flop
D – means Delay. The Q output always takes on the state of the D input at the moment of a rising clock edge.
The output takes the value of the D input or Data input, and Delays it by one clock count.
Truth Table | 
D | Q
0 | 0
1 | 1
Department of Computer Engineering

## Slide 8
T -Type Flip Flop (Toggle)
In J K Flip Flop , if J=K, the resulting Flip flop is referred to as a T- type Flip Flop.
T | Q
0 | Q
1 | Q’
Pr
Clk
Cr
Department of Computer Engineering

## Slide 9
Excitation Tables
Two tables are there:-
Truth table:- shows operation of circuits i.e. shows changes in output whenever changes in inputs. Mapping between input to output.
Excitation table:- Sometimes there is need to find input condition from the given output conditions, we need excitation table. In this case for the desired output, we need to find out input conditions
Department of Computer Engineering

## Slide 10
J K Flip Flop
JK truth table
Next state table
J | K | Qn+1
0 | 0 | Qn
0 | 1 | 0
1 | 0 | 1
1 | 1 | Qn’
Qn | Qn+1 | J | K
0 | 0 | 0 | X
0 | 1 | 1 | X
1 | 0 | X | 1
1 | 1 | X | 0
JK excitation table
J | K | Qn | Qn+1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Department of Computer Engineering

## Slide 11
SR truth table
Next state table
S | R | Qn+1
0 | 0 | Qn
0 | 1 | 0
1 | 0 | 1
1 | 1 | ?
Qn | Qn+1 | S | R
0 | 0 | 0 | X
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | X | 0
SR excitation table
S | R | Qn | Qn+1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | ?
1 | 1 | 1 | ?
S R Flip Flop
Department of Computer Engineering

## Slide 12
D truth table
Next state table
D | Qn+1
0 | 0
1 | 1
D excitation table
D | Qn | Qn+1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
Qn | Qn+1 | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
D Flip Flop
Department of Computer Engineering

## Slide 13
T truth table
Next state table
T | Qn+1
0 | Qn
1 | Qn’
T excitation table
T | Qn | Qn+1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Qn | Qn+1 | T
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
T Flip Flop
Department of Computer Engineering

## Slide 14
Thank you
Department of Computer Engineering