## Slide 1
Department of Computer Engineering
1
Sequential Logic Design – Truth Tables and Excitation Tables

## Slide 2: Points covered
Department of Computer Engineering
2
Introduction
Flip flop, truth table and excitation table
JK to D Flip flops
T to D Flip flop
SR flip flop to JK flip flop

## Slide 3: Department Vision & Mission
Department of Computer Engineering
Vision
Achieve academic excellence through education in computing, to create intellectual manpower to explore professional, higher educational and social opportunities.
Mission
To impart learning by educating students with conceptual knowledge and hands on practices using modern tools, FOSS technologies and competency skills there by igniting the young minds for innovative thinking, professional expertise and research.

## Slide 4
SR FF
IF S=R=0 Circuit will be same state i.e. No Change.
IF S=1 & R=0 then Q=1
IF S=0 & R=1 then Q=0
IF S=R=1 , then both the outputs Q and Q̅ will try to become 1 which is not allowed and therefore this input condition is prohibited
(Race Condition).
Department of Computer Engineering

## Slide 5: JK FF
Used to avoid race condition which does occur in SR FF
It has 2 inputs named J & K.
It has two outputs Q & Q’.
One Clock signal.
2 Asynchronous inputs PR & CLR
Symbol of JK -
Department of Computer Engineering

## Slide 6
JK FF Operation
J | K | Q | Q’ | Mode
0 | 0 | Q | Q’ | Hold
1 | 0 | 1 | 0 | Sets
0 | 1 | 0 | 1 | Resets
1 | 1 | Q’ | Q | Toggle
The 4 modes of operation are: hold, set, reset, toggle
Truth Table of JK
Department of Computer Engineering

## Slide 7
D-Type Flip Flop
D – means Delay. The Q output always takes on the state of the D input at the moment of a rising clock edge.
The output takes the value of the D input or Data input, and Delays it by one clock count.
Truth Table | 
D | Q
0 | 0
1 | 1
Department of Computer Engineering

## Slide 8
T -Type Flip Flop (Toggle)
In J K Flip Flop , if J=K, the resulting Flip flop is referred to as a T- type Flip Flop.
T | Q
0 | Q
1 | Q’
Pr
Clk
Cr
Department of Computer Engineering

## Slide 9
Excitation Tables
Two tables are there:-
Truth table:- shows operation of circuits i.e. shows changes in output whenever changes in inputs. Mapping between input to output.
Excitation table:- Sometimes there is need to find input condition from the given output conditions, we need excitation table. In this case for the desired output, we need to find out input conditions
Department of Computer Engineering

## Slide 10
J K Flip Flop
JK truth table
Next state table
J | K | Qn+1
0 | 0 | Qn
0 | 1 | 0
1 | 0 | 1
1 | 1 | Qn’
J | K | Qn | Qn+1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Department of Computer Engineering

## Slide 11
J K Flip Flop
JK truth table
J | K | Qn+1
0 | 0 | Qn
0 | 1 | 0
1 | 0 | 1
1 | 1 | Qn’
Qn | Qn+1 | J | K
0 | 0 | 0 | X
0 | 1 | 1 | X
1 | 0 | X | 1
1 | 1 | X | 0
JK excitation table
Department of Computer Engineering

## Slide 12
SR truth table
Next state table
S | R | Qn+1
0 | 0 | Qn
0 | 1 | 0
1 | 0 | 1
1 | 1 | ?
S | R | Qn | Qn+1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | ?
1 | 1 | 1 | ?
S R Flip Flop
Department of Computer Engineering

## Slide 13
SR truth table
S | R | Qn+1
0 | 0 | Qn
0 | 1 | 0
1 | 0 | 1
1 | 1 | ?
Qn | Qn+1 | S | R
0 | 0 | 0 | X
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | X | 0
SR excitation table
S R Flip Flop
Department of Computer Engineering

## Slide 14
D truth table
Next state table
D | Qn+1
0 | 0
1 | 1
D | Qn | Qn+1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
D Flip Flop
Department of Computer Engineering

## Slide 15
D truth table
D | Qn+1
0 | 0
1 | 1
D excitation table
Qn | Qn+1 | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
D Flip Flop
Department of Computer Engineering

## Slide 16
T truth table
Next state table
T | Qn+1
0 | Qn
1 | Qn’
T excitation table
T | Qn | Qn+1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Qn | Qn+1 | T
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
T Flip Flop
Department of Computer Engineering

## Slide 17
T truth table
T | Qn+1
0 | Qn
1 | Qn’
T excitation table
Qn | Qn+1 | T
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
T Flip Flop
Department of Computer Engineering

## Slide 18: Conversion of FF
Identify available and required flip flop
Make characteristic table for required flip flop.
Make excitation table for available flip flop.
Write Boolean expression for available flip flop.
Draw the circuit.
Department of Computer Engineering

## Slide 19: Conversion of JK to D Flip
1) available flip flop - JK
required flip flop - D
2) D truth/characteristics table (required FF)
D | Qn+1
0 | 0
1 | 1
Qn | Qn+1 | J | K
0 | 0 | 0 | X
0 | 1 | 1 | X
1 | 0 | X | 1
1 | 1 | X | 0
3) JK excitation table
Qn | D | Qn+1 | J | K
0 | 0 | 0 | 0 | X
0 | 1 | 1 | 1 | X
1 | 0 | 0 | X | 1
1 | 1 | 1 | X | 0
Write Boolean expression
0
Qn
X
X
1
D
0
1
0
1
x
Qn
1
0
x
D
0
1
0
1
J=D
K=D’
Department of Computer Engineering

## Slide 20: Conversion of T flip flop to D flip flop
1) available flip flop – T
required flip flop - D
2) T truth/characteristics table (required flip flop)
D | Qn+1
0 | 0
1 | 1
Qn | Qn+1 | T
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
3) T excitation table
Qn | D | Qn+1 | T
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Write Boolean expression
0
Qn
1
0
1
D
0
1
0
1
T=Q’ D + Q D’
= Q ⊕ D
Department of Computer Engineering

## Slide 21: Conversion of SR flip flop to JK flip flop
1) available flip flop – SR
required flip flop - JK
2) T truth/characteristics table (required flip flop)
Qn | Qn+1 | S | R
0 | 0 | 0 | X
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | X | 0
3) SR excitation table
Qn | J | K | Qn+1 | S | R
0 | 0 | 0 | 0 | 0 | X
0 | 0 | 1 | 0 | 0 | X
0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | X | 0
1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | X | 0
1 | 1 | 1 | 0 | 0 | 1
Write Boolean expression
J | K | Qn+1
0 | 0 | Qn
0 | 1 | 0
1 | 0 | 1
1 | 1 | Qn’
Qn
JK
00
01
11
10
0
1
0
0
1
1
X
0
0
X
S = Qn’. J
Qn
00
01
11
10
0
1
X
X
0
0
0
1
1
0
JK
R = Qn. K

## Slide 22
JK- Flip Flop to T- Flip Flop

## Slide 23
T Flip Flop to JK Flip Flop

## Slide 24
Thank you
Department of Computer Engineering